# South Dakota BOR

Northern State University

## Residence Hall Mattress Specification

QUANTITY - 10

We reserve the right to request a sample of product before committing to order

Product: Firmness Foam Mattress

- Mattress shall be fire-retardant per Federal Specification DOC-FF-4 72 and California Technical Bulletin #117.   Shall be dual foam with fire retardant outer cover.  Each Mattress is to be packed in individual polyethylene bags.

- Mattress shall be of the following nominal dimensions:

36” Width x 80” Length    This measurement is good.

Materials:

DUAL FIRMNESS FOAM MATTRESS

- Topper: 5 Zone 2-inch convoluted high density plush topper

- Core: 4-inch firm high density foam core

- Components bond together by a non-toxic water-based adhesive

- Cover: XP FR – FB 210Denier poly urethane coated nylon ticking with laminated FR Barrier

- Inverted seam lock stitch construction

- FR thread (fire retardant)

- All safety testing done by UL labs

- Mattress conforms to CFR 1632

- Mattress conforms to new CPSC 16 CFR 1633

- Mattress conforms to BFD IX-11 BC

- Mattress conforms to California Bureau of Home Furnishings Technical Bulletin 129 “Flammability Test Procedure for Mattresses for use in Public Buildings”

- Entire mattress must be recyclable

- No vents allowed because they can allow bed bug intrusion

- Shipped in 4 mil poly bags rolled or flat is acceptable

Tolerance:

- Commercial tolerances shall apply on all material and dimensions.

Warranties:

- A minimum of two (2) year warranty is acceptable on workmanship and material.   Excluded from this warranty will be misuse of mattress such as burns, chemicals, negligence, or improper cleaning.

Delivery:

- Delivery date no later than 07/25/2022

- Delivery will be coordinated with Larry Brunmaier, 605-216-0391

- Just on time Delivery is required, no early delivery.

- Delivery must be made during regular working hours of 8:00 AM to 4:00 PM

- Delivery Address:

  - Northern State University

  - 1200 S Jay Street

  - Aberdeen, SD  57401

- A 24-hour notice is requested for delivery.  Larry Brunmaier, 605-216-0391